## Slide 1: BIOE 498 / BIOE 599: Computational Systems Biology for Medical Applications CSE 599V: Advancing Biomedical Models Lecture 2: Modeling Essentials
Joseph L. Hellerstein*
Herbert Sauro**
*eScience Institute, Computer Science & Engineering
**BioEngineering

## Slide 2: G.P.E. Box (Famous Statistician)
All models are wrong.
But some models are useful.

## Slide 3: Agenda
Conceptual models
  Variable types, units, relationships
Dimensional analysis
Deterministic time course models
Stochastic time course models

## Slide 4: Refresher
What are we modeling?

## Slide 5: Running Example: Hydraulic Engineering
Reservoir provides public water
Water level
Flow rate
Streams fill reservoir
Flow rate
Lake provides recreation
Water level
Flow rate
Streams fill lake
Flow rate
Pipe provides lake water to reservoir
Flow rate

## Slide 6: The Problem
Maximize the height of the lake water subject to a minimum height of the reservoir water.
Most recreational benefit to public
Ensure delivery of quality water to public
Lake height
Reservoir height

## Slide 7: Element
Abstraction of a system component as a collection of related variables.
Flow:
Vessel:
Conduit:
Variables
Units
out = flow out
in = flow in
out = flow out
height = water height
setting = valve position
m = meters
m3s-1 = cubic meters per sec
m3s-1
m3s-1
m3s-1
in = flow in
out = flow out
rivers
lake
dam
pipe
m3s-1
= unitless

## Slide 8: A conceptual model relates inputs to outputs.
Flow:
Vessel:
Conduit:
Variables
out
in
out
height
setting
in
out
Conceptual
Model
unknown
function
unknown
function

## Slide 9: Conceptual Model
A conceptual model specifies how the inputs of one element relate to the outputs of other elements.
F1.out
V1.in
=
V1.height
V1.out
=
P.in
P.setting
P.out
F1
V1
P
F2
V2
+
F2.out
V2.in
V2.height
V2.out
Given F1.out, F2.out
Find V1.height, V2.height
Modeling objective

## Slide 10: The Vessel Black Box
How do we compute Vessel.height from Vessel.in and Vessel.out?
Modeling assumption
  Vessel is a cylinder with radius Vessel.radius, a model parameter
How is Vessel.radius estimated?
Vessel.in
Vessel.height
Vessel.out
Notes: A lake is not a cylinder. The model is wrong. But this can be a useful approximation.

## Slide 11: Technical Model for Vessel.height
Vessel.volume = Vessel.height*Pi*Vessel.radius2
dVessel.Volume = Vessel.out – Vessel.in
dVessel.height = (Vessel.out – Vessel.in)/(Pi*Vessel.radius2)
Integrate (sum) to calculate Vessel.height from dVessel.height.

## Slide 12: Simplified Modeling Workflow
System Diagram
Conceptual
Model
Technical
Model
F1.out
V1.in
=
V1.height
V1.out
=
P.in
P.setting
P.out
+
F2.out
V2.in
V2.height
dVessel.height = (Vessel.out – Vessel.in)/(Pi*Vessel.radius2)
V2.out

## Slide 13: Vessel, Flow -> Species, Reactions
Relate to reactions
Show units
Conceptual model relates to metabolism
  But box is for enzyme, not function

## Slide 14: Dimensional Analysis

## Slide 15: Lac Operon

## Slide 16: Technical Models With Differentials

## Slide 17: Technical Models With Stochastics

## Slide 18: Learning Objectives
Conceptual models
  Construct appropriate element abstractions of a system, their variables, and the relationships between variables